## Slide 1: TOUCHPAD
Embedded Design
Techkriti’11
Neeraj Kulkarni
Anurag Sai

## Slide 2: Introduction
Current technologies of touchpad based on different methods of sensing include capacitive touchpad, resistive touchpad etc.
In our project we are implementing a method in which the touch sensing is done using a grid of wires.
Along with single-touch sensing we have also implemented multi-touch feature.

## Slide 3: Hardware:
Components:
  Touchpad: Wire grid of 8X8 dimension.
  Atmega MCU
  UART communication module.
Touch sensing:
  Horizontal wires -pulled up at logic 1 Vertical wires-cyclically given logic 0 at a very high frequency of MCU.
  Intersection points in grid - sensing points
Multi-touch:
  The above method of touch sensing also allows us to achieve Multi-Touch.
  Record the Touch points in each cycle. Then process the data according to the multi touch application required.

## Slide 4: Hardware Interface:
Data to be sent to PC from Hardware:
Position Co-ordinates of pointer:
Essentially the co-ordinates of touch points.
Events:
  Click: Particular touch point is pressed for less than some few milliseconds.
  Double-Click: Click pressed twice.
  Drag : A click and then mouse motion.
  Multi-Touch Applications: Various Patterns like scroll, zoom-in, zoom-out etc.
  Communication between Hardware and PC:
  Data sent by UART communication.

## Slide 5: Software
Reading data
  Receive data in CV-AVR and save as .txt file. The file is read in MATLAB.
Various patterns detected using image processing in MATLAB.
  Received pattern is stored in a matrix. The path is plotted.
  Saving it as an image.
  Converting into binary image.

## Slide 6
Error management.
  Path of the finger is highly erroneous.
  Changes in data stored to make the pattern neat, yet retaining its shape.
Properties analyzed
  Image properties like number of lines, slopes, location, Intersection points are analyzed to determine a particular pattern.
  Deciding the action to be done based on the pattern detected.
Mouse motion achieved using Robot class of JAVA.
  Key Press.
  Mouse movement.

## Slide 7: Special features
Smooth mouse motion.
Single click, Double click and Drag.
Patterns: To make it user-friendly
  Cross (X) – Close the existing window.
  Circle (O) – Rotate images (Clock-wise & Counter clock-wise).
  Diverging lines – Zoom in.
  Converging lines – Zoom out.
  Scroll (|) – Scroll through pages.
  Right, Left – Scroll through images.
  Alt + Tab (_) – Scroll through various windows.
  Snapshot (||) –Take a screenshot.
  Alphabet (A) – Type text.

## Slide 8: Problems Faced:
Hardware:
Unnecessary shorting/touching of 2 wires:
  When 1 point is pressed the 1 beside was also getting shorted.
  Solution: Placing an insulating material between the horizontal and vertical set of wires.
Deformation of shape of wires:
  When pressed a number of times the wire got deformed thus establishing a continuous touch.
  Solution: Using a fairly flexible wire.
Events for Multi-Touch application:
  Difficulty was faced in determining ‘event’ data for various patterns.
  Solution: Coding though a bit involved.

## Slide 9
Software:
Interfacing with MATLAB
  Timeout error
  Solution : Store the data in a .txt file and read it in MATLAB
Errors in pattern
  Passing a finger in between different points gives unpredictable pattern.
  Solution : Linear approximation.
Discrete mouse motion
  Mapping a 8*8 matrix into a small square on the screen. Only 64 possible positions of mouse.
  Increasing size of the square decreases accessible area on screen.
  Solution : Linear approximation. Smooth continuous motion

## Slide 10: Scope for improvement
Denser grid. More sensing points.
  Number of accessible points can be increased. Distance travelled by mouse per unit change in sensing points can be decreased. Results in a continuous motion.
Typing text.
  Increase the number of detectable patterns. Include Alphabet so as to type text using touchpad !!
Convert .m file to .exe file.
  This removes the requirement of MATLAB on the PC.
Implement wireless UART communication.
  Move around carrying the touchpad and still be able to access it.

## Slide 11: Cost Estimation
ITEM | COST
Atmega-16 | Rs.140/-
Programmer | Rs.100/-
USB to Serial connector | Rs.120/-
Touchpad | Rs.30/-
TOTAL COST : Rs.390/-